## Slide 1: MSDAP Final Presentation
Lamin Jammeh (DAL852207)
Caleb Perez (CXP180012)

## Slide 2: MSDAP Architecture
Datapath
Memories
Controller

## Slide 3: MSDAP Architecture
Built as a hearing aid that processes input audio and outputs filtered audio to the user using a digital FIR convolution.
  High priority is low power consumption, as it is not meant to be plugged in and will run on a small battery.
Two-process circuit
  Keeps data path and control paths separate and distinct. (Previous slide)
Both Main Controller and ALU Controller are FSMs.
  Allows for easy and distinct input-based control of the outputs.
Layout must be as small as possible as it should fit within the ear.

## Slide 4: Original Code
Our original code was validated as far as State 6.
  This means that we were able to store and recall data from the memories accordingly.
Could not get a proper output through the ALU data path.
  Due to lack of proficiency in coding Verilog. Could not properly execute ALU sub-block actions in order.

## Slide 5: Original Code Simulations
Here we can see that our original code was successful in processing the initial RJ, Coeff, and Input Data, as well as providing said data while the ALU is attempting to process data.
We did make a testbench for the MSDAP, as well as testbenches for every block. This waveform is from the MSDAP testbench.
RJ Processing
Coeff Processing
Data Processing
RJ Readback into ALU

## Slide 6: Utilization of Provided Code
Decision was made to utilize code provided by the TA.
Would allow us to continue with layout and finish the project.
Verified provided code output by comparing given data1.out to generated data1.out (Snippet shown on the right)
Generated:
Expected:

## Slide 7: Differences in Provided Code and Original
Our ALU Controller Code
Provided ALU Controller Code
Too many states! Overcomplicated

## Slide 8: Differences in Provided Code and Original
Our ALU Controller Code
Provided ALU Controller Code
Incorrect activation of ALU data path.
Many more differences in how data was handled, but the ALU was where our original code failed. Overall, the provided code runs faster and is less bloated.

## Slide 9: Constraints for synthesis
Clock constraints
  Clock uncertainty for both Dclk and Sclk is +/-100ps
  Dclk and Sclk period = 1302000.0ps and 3333.3ps respectively
Pin constraint
  All loads set to 1pf
Floorplan constraint: this is important to make sure need instance don’t flattened or synthesize to induvial cells
  All memories a plan as instance
  The tool command instructions needs preserve all SRAMs

## Slide 10: Tool commands used for Synthesis
set_db [get_designs SRAM1RW128x12] .dont_touch true
set_db [get_designs SRAM1RW128x12] .is_blackbox true
set_db [get_designs SRAM1RW256x8] .dont_touch true
set_db [get_designs SRAM1RW256x8] .is_blackbox true
set_db [get_designs SRAM2RW16x8] .dont_touch true
set_db [get_designs SRAM2RW16x8] .is_blackbox true
# 6. Elaborate top design
set_db [get_designs MSDAP] .auto_ungroup none
set_db [get_designs R_MEM] .auto_ungroup none
set_db [get_designs DATA_MEM] .auto_ungroup none
set_db [get_designs CO_MEM] .auto_ungroup none
The intension for the Floorplan is to place all memories as induvial components (use as given)
don’t_touch and is_blackbox prevents the SRAMs from getting flattened or synthesize into individual gates
To preserve hierarchy the auto_ungroup has been disabled for the R, Data, and Co modules

## Slide 11: Preserve mem instances
# Auto-preserve only memory SRAM instances (not inner registers)
foreach cell [concat \
[get_cells -hierarchical *mem_0_0] \
[get_cells -hierarchical *mem_0_1] \
[get_cells -hierarchical *mem_0_2] \
[get_cells -hierarchical *mem_0_3] \
] {
if {[llength [get_cells -quiet $cell]] > 0} {
set_db $cell .preserve size_ok
puts "Preserved: $cell"
}
}
The following are preserve as instances for easy placement.
  Mem_0_0
  Mem_0_2
  Mem_0_2
  Mem_0_3

## Slide 12: Syn area report

## Slide 13: Syn Power report

## Slide 14: Syn Timing/ setup report

## Slide 15: Syn PPA
PPA | Value
Power | 5.488410319 mW
Performance | 33333 ps = 30 MHz
Area | 564864 µm²

## Slide 16: Place and Route Process Flow
Setup Environment
  Set Process node for the circuit
  Set timing constraints
  Define the timing scale
  Include lib exchange file for all cells in the netlist
  Define all corners to set chip behavior under different conditions
Read Design netlist and define the top module in the netlist
Define your Power parameters (VDD and VSS)
Exclude cells that may cause issues

## Slide 17: PnR Process Flow continues
Source floorplan
  Make overall chip area is largeenough to fit all instance

## Slide 18: Add physical constraints
Define physical contraint before placing Power rails
  Define pith and offset rules
  Add Via Rules
  Define if via on IO pads are allowed
  Add blockages or keepers to all corners of the chip

## Slide 19: Placement
Add tap cells
Add Power Strapes
Place I/O pins
Place cells
Define clock tree
Define Keepouts for easy routing before adding filler cells

## Slide 20: Route Design
Route using global_detail to help reduce DRC violations

## Slide 21: Create the needed file for the next Process
Generate a def file for orphyiscal implementation
Generate a netlist for lvs that contains only the transistor level description of the desing without any physical description

## Slide 22: Design Report (Area)

## Slide 23: Design Report (Power)

## Slide 24: Design Report (Setup/timing)

## Slide 25
PPA after PNR
PPA | Value
Power | 0.19334916 mW
Performance | 33326.020 ps = 30.011 MHz
Area (Design_area + cell_area) | 51150.28 µm²

## Slide 26: PPA Syn vs PnR
PPA | Syn Values | PnR Values
Power | 5.488410319 mW | 0.19334916 mW
Performance | 33333 ps = 30 MHz | 33326.020 ps = 30.011 MHz
Area (Design_area + cell_area) | 564864 µm² | 51150.28 µm²

## Slide 27: DRC report
Tota DRC errors = 371
Types of errors
  ViaEnclosure violation
  EndofLine violation
Error location
  All errors happened around the SRAM macros
Reason: via rules define in the tool command did not apply to the macro sine the macros are define as instances (use as it is)

## Slide 28: LVS errors