## Slide 1: Verilog Design Structural Design
EE417 Logic Design Using FPGAs

## Slide 2: Introduction to VERILOG
Every logic design entity in Verilog is presented as a module.
A Verilog module has the following format:
module module_name (List of ports separated by commas);
input and output declarations;
module functionality
endmodule

## Slide 3: Introduction to VERILOG
Verilog modules
The functionality of each module can be defined using three modeling levels:
1. Structural or gate level
2. Dataflow level
3. Behavioral or algorithmic level
Verilog allows different levels of abstraction to be mixed in the same module.

## Slide 4
Data Types Used:
Single-bits or Bit-vectors are defined in Verilog.
wire s single-bit
wire [7:0] bus bit-vector
Each bit can take one of the following values:
‘1’ A logic one
‘0’ A logic zero
‘Z’ High impedance, floating.
‘X’ Unknown logic value (or don’t care). An X bit might be a 0, 1, Z, or in transition. In the simulation waveform viewer, Unknown signals are RED. You should avoid unknown values after reset.

## Slide 5
Bit-Vectors
A net or register can be declared as a vector
wire [7:0] bus;
wire [31:0] busA, busB, busC;
It is possible to access bits or parts of vectors
bus [7]
busA [2:0]
busC [0:2]

## Slide 6: 1. Structural Modeling
In structural modeling, digital design functions are defined by the arrangement of building blocks (basic logic gates or modules), and their connections together.
Nets represent the connections between hardware elements. They are continuously driven by the output of connected devices. They are declared using the keyword wire.
wire s1;
wire c1, c2;

## Slide 7
module FullAdder (S, Cout, A, B, Cin);
input A, B, Cin;
output S, Cout;
reg S, Cout;
…
endmodule
All ports declarations (input, output, inout) are implicitly declared as wires.
If an output should hold its value, it must be declared as reg.
Declaring the ports:

## Slide 8
module FullAdder (output reg S, output reg Cout, input A, input B, input Cin);
…
endmodule
Declaring the ports:

## Slide 9
Gate level Modeling
wire z, z1, OUT, OUT1, OUT2, IN1, IN2
and a1(OUT1, IN1, IN2);
nand na1(OUT2, IN1, IN2);
xor x1(OUT, OUT1, OUT2);
not (z, OUT);
buf final (z1, z);
The gate level modeling describes the topology of the circuit
All instances are executed concurrently just as in hardware
Instance name is optional
The order of the inputs and outputs follow the format used to define the gate (output then list of inputs).
Instantiation of the gate module
Instance name

## Slide 10: EXAMPLE: 1-bit full adder
Write down the Verilog code specifying the design of the shown 1-bit full adder.
Create the Truth table for the full adder and specify the correct output for every possible combination of inputs.

## Slide 11
module fullAdder (S, Cout, A, B, Cin);
input A, B, Cin;
output S, Cout;
wire s1, c1, c2;
xor xor_1 (s1, A, B);
xor xor_2 (S, s1, Cin);
and and_1 (c1,s1, Cin);
and and_2 (c2,A,B);
or or_1 (Cout, c1, c2);
endmodule
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 12
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Cin\AB | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
For S:
This is S from the circuit diagram given.
De Morgan Rule

## Slide 13
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Cin\AB | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 1
For Cout:
From the circuit diagram given

## Slide 14: Example
module adder( input [3:0] a_i,
input [3:0] b_i,
output cy_o,
output [3:0] sum_o );
// HDL modeling of adder functionality
// a single line with comments
/* multiple lines or block
comments */
endmodule
Ports must have a direction and a bit-width.
As a programming style you can use
_i to denote input variables and _o to denote output variables.
The single line comments follow two forward slashes //
And block comments are included between /* */

## Slide 15: Module Instantiation
We can build a larger module by instantiating other modules.
For example a 4-bit full adder can be designed by connecting 4 modules of the full adder that we designed.
B[3:0]
A[3:0]
Sum[3:0]
Carry
B[3]
A[3]
Sum[3]
Carry
B[2]
A[2]
Sum[2]
C2
B[1]
A[1]
Sum[1]
Cin[0]
B[0]
A[0]
Sum[0]
C0
C1

## Slide 16: Module Instantiation:
We can connect module instances either by:
The order in the ports’ list
The name of the port.

## Slide 17
module adder( input [3:0] A, B,
input Cin,
output Carry,
output [3:0] Sum );
wire c0, c1, c2;
FA fa0( A[0], B[0], Cin, c0, Sum[0] );
FA fa1( A[1], B[1], c0, c1, Sum[1] );
FA fa2( A[2], B[2], c1, c2, Sum[2] );
FA fa3( A[3], B[3], c2, Carry, Sum[3] );
endmodule
module FA ( input a_i, b_i, cy_i
output cy_o, sum_o);
// HDL modeling of 1 bit full adder functionality
endmodule
Connecting Instantiated modules using the order of the ports list:

## Slide 18
module adder( input [3:0] A, B,
input Cin,
output carry,
output [3:0] sum );
wire c0, c1, c2;
FA fa0 ( .a_i (A[0]) ,
.b_i (B[0]) ,
.cy_i (Cin) ,
.cy_o (c0) ,
.sum_o (Sum[0]) );
...
endmodule
module FA ( input a_i, b_i, cy_i
output cy_o, sum_o);
// HDL modeling of 1 bit full adder functionality
endmodule
The order of the ports in the list in this case is not important.
Connecting Instantiated modules using the names of the ports:

## Slide 19
VERILOG NUMBER FORMATS:
<size>’<base format><number>
Specifies the number of bits used to save the number
D or d for decimal
H or h for hexadecimal
B or b for binary
O or o for octal
The number specified using the base format used.
X or x is used for don’t cares
Z or z is used for high impedance
_ used for readability

## Slide 20
Verilog Number Format:
<size>’<base format><number>
138 // decimal number, 32 bit as 00000000000000000000000010001010
10′d138 // decimal number, 10 bit as 00_1000_1010
6′o74 // octal number, 6 bits as 111100
24′h25F // hexadecimal number, 24 bit as 000000000000001001011111
8′hxB // hexadecimal number, 8 bit as xxxx1011
3′b010 // binary number, 3 bits as 010
5′d124 // decimal number, 5 bits as 11100 since 7 bits are required
12′oF2 // invalid, F is not an octal digit

## Slide 21: Verilog Constants
Constants in Verilog are declared with the keyword parameter and can include arithmetic expressions with other constants. The keyword defparam is used to redefine a parameter within a module. The redefinition can be specifically applied to the parameters of a specific nested module.
parameter BUS_WIDTH = 32; // integer
parameter XMAX=640, YMAX = 480; // integers
parameter SIZE = XMAX*YMAX; // arithmetic expression
// redefinition of BUS-WIDTH in instance M2 of nested module auxbus
defparam auxbus.M2.BUS_WIDTH = 16;

## Slide 22: Verilog Wires
The net variable type wire establishes behavioral connectivity with logic values of 0, 1, x (unknown) or z (high impedance) determined by the module port that drives the signal variable.
wire glbrst; // scalar net signal
wire mclk, dav; // scalar net signals
wire [31:0] average; // 32-bit vector net signal

## Slide 23: Verilog Register Variables
The integer type of register variable supports numerical computation in Verilog behavioral synthesis. Integer variables are declared by the keyword integer, have a default fixed size of 32 bits in signed two’s complement format and a default initial value of zero.
Integers are true abstractions that must have a numerical value, but the procedures that they comprise are compiled by the Verilog HDL to synthesizable hardware.
integer data; // integer
integer i, j, k; // multiple
integer data[1:1000] // integer array

## Slide 24: Verilog Register Variables
Register variables are used in behavioral modeling, are assigned values by procedural statements and store information. Register variables that are used in a Verilog HDL behavioral description are declared by the keywords reg or integer.
The keyword reg is the abstraction of a hardware storage element and has a default size of one bit and an initial logic value of x (unknown).
reg clock; // register signal
reg reset, read_data; // register signals
reg signed [7:0] sum; // 7-bit plus sign register signal
reg [3:0] data = {adata[1:0], bdata[1:0]}; // concatenation

## Slide 25: Verilog String Variables
Verilog utilizes the register variable with the reg declaration to store ASCII character strings as 8-bit values. The string can be initially assigned to the register variable reg declaration by enclosing it within quotation marks. If the string assignment uses less than the available number of bits, the unused register variable reg declaration bits are filled with zero.
parameter STRING_LENGTH = 11; // parameter declaration
reg [8 * STRING_LENGTH] string_data; // arithmetic calculation of size
reg [7:0] byte_memory [0:511]; // 512 byte memory
strdata = ”hello world”; // string assignment to a register