## Slide 1: Verilog Design Dataflow modeling Design
EE417 Logic Design Using FPGAs

## Slide 2: 2. Dataflow modeling
A module is designed by specifying the data flow, where the designer is aware of how data flows between the hardware registers and how the data is processed in the design. The continuous assignment is one of the main constructs used in dataflow modeling.
assign out = i1&i2;
assign addr[15:0] = addr1[15:0] ^ addr2[15:0];
assign {c_out , sum[3:0]} = a[3:0] + b[3:0] + c_in;
A continuous assignment is always active and the assignment expression is evaluated as soon as one of the right-hand-side variables changes.
Assign statements describe hardware that operates concurrently − the order does not matter.
Left-hand side must be a vector net. Right-hand side operands can be wires, registers, integers, and reals.

## Slide 3: Operator types in dataflow expressions
Verilog Bitwise Signal Operations
Verilog Reduction Operations
Verilog Logical Operations
Verilog Relational Operations
Verilog Equality Operations
Verilog Logical Shift Operations
Verilog Arithmetic Shift Operations
Verilog Arithmetic Operations
Verilog Conditional Operations

## Slide 4
Verilog Bitwise Signal Operations:
Verilog provides intrinsic signal operations which describe logic symbolically in behavioral synthesis, rather than by Verilog primitives in a structural model which utilize combinational logic gates.
The bitwise operators combine two signal operands to form a signal result.
~ Negation (one’s complement)
& And
| Or
^ Exclusive Or
~ ^ Exclusive NOR
^ ~ Exclusive NOR

## Slide 5
Verilog Reduction Operations
The reduction operators produce a scalar with logic values of 0, 1, or x (unknown) from a single signal operand. Each bit of the signal operand participates in the reduction operation to produce the result.
For example, if y = 1001, then &y = 0 and |y =1. The scalar value is x (unknown) if the operand contains at least a single bit which is unknown.
& And
~ & NAnd
| Or
~ | NOR
^ XOR
~ ^ Exclusive NOR
^ ~ Exclusive NOR

## Slide 6
Verilog Logical Operations:
The logical operators are similar to the reduction operators but produce a scalar with logic values of 0, 1, or x (unknown) from two signal operands. Each bit of the two signal operands participates in the logical operation to produce the result.
The scalar value is x (unknown) if either of the operands contains at least a single bit which is unknown. The operation is evaluated from left to right and ends as soon as the result is unequivocally true or false.
& & Logical And
| | Logical Or
For example, if x = 1001and y = 0110 then x && y = 0 and x || y = 1.

## Slide 7
Verilog Relational Operations:
The relational operators compare two signal operands and produce a scalar with logic values of 0 (false), 1 (true), or x (unknown).
The scalar value is x (unknown) if either operand contains at least a single bit which is unknown or z (high impedance).
< Less Than
< = Less Than or Equal To
> Greater Than
> = Greater Than or Equal To

## Slide 8
Verilog Equality Operations:
The logical equality and logical inequality operators compare two signal operands
bit-by-bit and produce a scalar with logic values of 0(false), 1 (true), or x (unknown).
The scalar value is x (unknown) if the operand contains at least a single bit which is unknown or z (high impedance).
= = Logical Equality
! = Logical Inequality

## Slide 9
Verilog Equality Operations:
The case equality and case inequality operators compare two signal operands bit-by-bit utilizing the four logic values (0, 1, x, z) and produce a scalar with logic values of 0 (false) and 1 (true).
= = = Case Equality
! = = Case Inequality

## Slide 10
Verilog Logical Shift Operations:
The logical shift operator shifts the bits in a signal operand to the right or left and fills the vacated bits with a logic value of 0.
> > Logical Shift Right
< < Logical Shift Left
For example, if x = 00011100 then x << 2 = 01110000.
if x = 10011100 then x << 2 = 01110000.

## Slide 11
Verilog Arithmetic Shift Operations:
Verilog supports the arithmetic shift operator which shifts the bits in a signal to the right or left and fills the vacated bits with the most significant bit (MSB) if a right shift and a logic value of 0 if a left shift. The left shift arithmetic operator is functionally the same as the left shift logical operator. The arithmetic shift right impolement sign extension.
For example, if x = 10011100 then x >>> 2 = 11100111.
> > > Arithmetic Shift Right
< < < Arithmetic Shift Left

## Slide 12
EXAMPLE:
A shift right operation represents a division by powers of 2
Verify that with the following numbers:
1111_0000 >>> 2
1110_0000 <<< 2
1_1010 >>> 1
0_0111 >>> 2
0_0010 <<< 2

## Slide 13
Verilog Arithmetic Operations:
The common arithmetic operations in Verilog manipulate the register variable reg declaration as signed or unsigned integers of any bit size.
The keyword signed is used to declare that the register variable reg declaration is signed. The register variable integer declaration has a default fixed size of 32 bits for signed two’s complement arithmetic.
* Multiplication
/ Division
% Modulus (Remainder)
+ Addition
– Subtraction

## Slide 14
Verilog Conditional Operations:
The conditional operation in Verilog can utilize the logic true or false of a Boolean expression to select one of two possible arithmetic expressions.
The form of the conditional operation is:
<Boolean expression> ? <result if true> : <result if false>
reg signed [15:0] c;
reg signed [7:0] a;
reg signed [7:0] b;
c = (a > b) ? 1 : 0; // c will be either 1 or 0
c = (a == b) ? a – b : a + b; // c will be either a – b or a + b
c = (a – b) > 4 ? a : b; // c will be either a or b

## Slide 15
Verilog Concatenation Operator
The concatenation is the combination of two or more signals
The concatenation is expressed by the brace characters {} bracketing two or more expressions separated by commas. {signal_1, signal_2}
reg [7:0] a, b; x = {a, 4'b1110, b[2:1]}
Result of this expression has 14-bits ('a' has 8 bits, 4'b1110 has 4 bits, b[2:1] has 2 bits).
Concatenations can also be expressed using a replication multiplier, which duplicates the expression it contains the number of times specified by the constant that precedes it. {replication_multiplier{expression}}
{a, {2{b, c, d}}, a}
The above concatenation is equivalent to the following concatenation: {a, b, c, d, b, c, d, a}

## Slide 16
EXAMPLE:
module mux2to1(s,a,b,y)
output y;
input s, a, b;
assign y = (b&s) | (a&s);
// or we can describe the mux as follows:
// assign y = s ? b : a;
endmodule

## Slide 17: Example
Write down a Verilog module code for a 4-1 multiplexer.