## Slide 1: Verilog Design Datapath-controller
EE417 Logic Design Using FPGAs
Reference: Advanced Digital Design with the VERILOG HDL (Michael Ciletti)

## Slide 2
The Data-path:
The datapath units consist of computational resources (adders, subtractors, multipliers, digital signal processors), logic for moving data through a system and between the computation units and the internal registers (multiplexers, decoders, encoders), and datapaths for moving data to and from the external environment.
The control unit:
The control unit is usually a FSM that orchestrate, coordinate, and synchronize the operations of datapath. The control unit of a system generate the signals that load, read, and shift contents of storage registers, steer signals through muxes, and control the type of operations though arithmetic units.

## Slide 3
Finite-State Machine
Data-path Logic
Data-path Registers
Control signals
Status signals
Data-path
clock
clock
External Control Inputs
Control Unit
Data-path Unit
Data-path

## Slide 4: Design example: Binary counter
Consider a synchronous 4-bit binary counter that is to be incremented by a count of 1 at each active edge of the clock, and whose count is to wrap around to 0 when the count reaches 1111. The counter should have a reset input that when enabled resets the count back to 0000. The counter also has an enable signal, if inactive, the counter should stop at the most recent count value reached when it was enabled.

## Slide 5
A different approach would be partitioning the machine into an architecture of separate datapath and control units as follows:
Control Unit
Count Register
MUX
+
count
1
enable
clock
reset
Data-path Unit
Binary Counter Architecture